## Slide 1: HYD FCX2027C
VERSION 3 / FEBRUARY 2020
HDPE Pipe
Handling
Notes: SG N/A
Instruction
Welcome students to class
Facilitator introduces self by stating
  your position at FMI
  how long you have worked for FMI
  how long you have worked in mining
Ask students what they want from the course
  Discuss what they want to gain from the course
  WIFM – “What’s in it for me?”
  This increase engagement by getting students vocalizing their opinions from the start of the course
  This increases motivation by showing students their ideas matter
  Option – Write down or remember what they want to learn. In a few slides, connect their responses to the learning objectives

## Slide 2
Expectations
Before We Start
Safety
Breaks/Restrooms
Technology
Participation
Class Ground Rules
Notes: SG N/A
Instruction
Administrative/Classroom policies
  Safety – Identify items such as evacuation procedures, gathering areas, emergency exits, and fire extinguisher locations
  Breaks and Restrooms
    Establish and announce a break schedule to the class. Take breaks after about every hour of instruction
    Identify the location of restrooms and smoking areas
  Technology policy – Review expectations on cell phone and laptop use during the training
  Participation
    This course requires significant participation
    Students should be prepared for discussions and small group activities
  Class ground rules – Verbalize expectations. Suggestions include
    Participate
    Be on time
    Stay on task
    Listen when others talk
    Respect the opinions and attitudes of others
  Student Course Evaluation
    Direct students to the Student Course Evaluation at the end of the SG
    Tell students to work on this throughout the course
    This helps students write ideas down as they have them
    Filling it out as they go, also helps gather more substantial feedback as they are not rushed to complete the entire evaluation at the conclusion of the course when they are anxious to leave

## Slide 3
Directions
Participate in an activity getting to know each other
Icebreaker
Activity 1
Notes: SG N/A
Time
Approximately 10 minutes
Materials
Choose an icebreaker from the FG and gather appropriate materials
Purpose
Successful icebreakers encourage students to contribute ideas and experiences thus increasing motivation and engagement in the class
The FG has many icebreakers to use now, after breaks, or any other time

## Slide 4
Assessment
Directions
Complete the Knowledge Pre-Assessment
Grade assessments as a class
Return assessments to facilitator
Knowledge Pre-Assessment
Notes: SG N/A
Instruction
The knowledge pre-assessment helps gauge student knowledge coming into the course
Give students about 30 minutes to complete
Grade as a class
Collect assessments
Compare these scores to the knowledge post-assessment at the end of the course to determine each student’s increase in knowledge

## Slide 5
Learning Objectives
SG iii
Module 1: Introduction
Describe the history and purpose behind FXC-HS12
Notes: SG page iii
Instruction
State objective(s) for each module
Learning objectives are also located at the beginning of each module
Option – If you wrote down or remember the student’s ideas of what they want to learn in the course, connect each response they gave to an objective (even if it’s a vague connection). This increases motivation by showing students their ideas matter

## Slide 6
Learning Objectives
SG iii
Module 2: Risk Management
Describe the purpose and process for hazard recognition before performing tasks related to working with HDPE Pipe
Identify the personnel who will be associated with the task, as well as their roles and responsibilities, to ensure the task is being performed safely and all involved abide by the policy
Notes: SG page iii
Instruction
State objective(s) for each module
Learning objectives are also located at the beginning of each module
Option – If you wrote down or remember the student’s ideas of what they want to learn in the course, connect each response they gave to an objective (even if it’s a vague connection). This increases motivation by showing students their ideas matter

## Slide 7
Learning Objectives
SG iii
Module 3: Pipe Handling
Describe safe practices and requirements of FCX-HS12 regarding receiving, loading, unloading, and storage of HDPE Pipe on FCX properties
Identify when to use the Receiving/Loading/Unloading Checklist, and describe how to fill out this form correctly
Notes: SG page iii
Instruction
State objective(s) for each module
Learning objectives are also located at the beginning of each module
Option – If you wrote down or remember the student’s ideas of what they want to learn in the course, connect each response they gave to an objective (even if it’s a vague connection). This increases motivation by showing students their ideas matter

## Slide 8
Learning Objectives
SG iii
Module 3: Pipe Handling (cont’d)
Identify the difference between a properly loaded shipment of HDPE Pipe and one that does not comply with the company’s shipping standards
Describe the procedure in place to report loads that do not meet company standards
Describe how to safely store HDPE Pipe according to policy requirements
Notes: SG page iii
Instruction
State objective(s) for each module
Learning objectives are also located at the beginning of each module
Option – If you wrote down or remember the student’s ideas of what they want to learn in the course, connect each response they gave to an objective (even if it’s a vague connection). This increases motivation by showing students their ideas matter

## Slide 9
Learning Objectives
SG iii
Module 4: Rigging
Describe the proper procedures required to safely pull various sizes and lengths of HDPE Pipe according to policy requirements
Identify the proper equipment required for the task
Identify appropriate forms for the tasks that will be performed and describe how to fill these forms out correctly
Notes: SG page iii
Instruction
State objective(s) for each module
Learning objectives are also located at the beginning of each module
Option – If you wrote down or remember the student’s ideas of what they want to learn in the course, connect each response they gave to an objective (even if it’s a vague connection). This increases motivation by showing students their ideas matter

## Slide 10
Learning Objectives
SG iv
Module 5: Fusing and Data Loggers
Identify the hazards associated with fusing, installation, and repair of HDPE Pipe as they relate to the FCX-HS12 policy and describe the proper procedures in place to mitigate those hazards
Notes: SG page iv
Instruction
State objective(s) for each module
Learning objectives are also located at the beginning of each module
Option – If you wrote down or remember the student’s ideas of what they want to learn in the course, connect each response they gave to an objective (even if it’s a vague connection). This increases motivation by showing students their ideas matter

## Slide 11
Learning Objectives
SG iv
Module 6: Audits and Training
Define the roles and responsibilities of the Corporate and site Pipe Safety Steering Teams
Explain the training requirements needed to safely handle or participate in the handling of HDPE Pipe
Notes: SG page iv
Instruction
State objective(s) for each module
Learning objectives are also located at the beginning of each module
Option – If you wrote down or remember the student’s ideas of what they want to learn in the course, connect each response they gave to an objective (even if it’s a vague connection). This increases motivation by showing students their ideas matter

## Slide 12
Introduction
SG V
Committed to health and safety of employees
Development of FCX-HS12
Purpose of training
One page policy document
Notes: SG page v
Instruction
Committed to health and safety
Freeport-McMoRan Inc. is committed to the health and safety of its employees
The Corporate Safety and Health Policy expresses this well: “We consider safety and health programs, both on and off the job, to be an investment in our most valuable resource – our employees”
With this in mind, it is important to note not only is the company taking responsibility for the safety of its employees, they also recognize proper training and personal responsibility are critical components to this
Development of FCX-HS12
Due to the stored energy and potential hazards related to working with High-Density Polyethylene (HDPE) Pipe
  Collaborative team methodically designed FCX-HS12 to address:
    Potential hazards and
    Mandated critical controls in order to mitigate the potential hazards from affecting the employees
  It was determined all employees and contractors who must work with this pipe be trained in all related aspects of technical skills and procedures, as well as health and safety factors
  It is essential employees follow all facets of FCX-HS12
Purpose of training
  Ensure anyone who will work with HDPE Pipe has been trained according to HDPE Pipe Handling Policy (FCX-HS12) prior to performing that work
  Policy does not cover every aspect of handling HDPE Pipe
    If at any time someone has questions related to the work, they have an obligation to stop the job and seek out clarification.
    There are many forms and permits designed to help the teams plan and execute their jobs safely
    These forms and permits will be presented during this training
    The goal is for all to go home safely each day
Discuss the one page policy document on the next slide

## Slide 13
One Page HDPE Pipe Handling Policy
Notes: SG page v
Instruction
Developed in accordance, with
  HDPE Pipe Handling Policy – FCX-HS12 (One Page)
  Administration Policy – FCX-HS01
  Technical Supplements
  Administration Standard Glossary
Located on the main website under Health and Safety > Policies (H&S Policies) > HDPE Pipe Handling

## Slide 14
Fatal Risk and Critical Controls
SG vi
Fatal Risk Management Program
Fatal Risk – uncontrolled risk that will kill you
Critical Control – implemented to eliminate or reduce the risk for a task/job
Notes: SG page vi
Instruction
Fatal Risk Management
  Continuation of the Fatality Prevention Program
  Focus is placed on identifying Fatal Risks and Critical Controls in an attempt to safeguard all employees
  Standardizes communication for twenty-three Fatal Risks by implementing icons, definitions, and Critical Controls.
Fatal Risks are based on safety issues that have resulted in catastrophic events such as severe injury or death.
For each identified Fatal Risk a list of necessary Critical Controls was developed to prevent or mitigate the most serious consequences of these risks. Once the Fatal Risk is identified, applying the most effective Critical Control is crucial.
A Critical Control is a device, system, or process implemented to eliminate or reduce the risk for a task/job, and if missing or overlooked has the potential to lead to catastrophic outcomes such as serious injury or death.
  These Critical Controls are considered the most impactful on preventing a fatality or injury and have been previously established based on data.
  The absence or failure of a Critical Control significantly increases the risk of severe injury or death despite the existence of other controls.
The Fatal Risk(s) and Critical Controls relevant to this course are provided next.

## Slide 15
Lifting Operations
SG vi
Loss of control of load suspended by lifting equipment
Critical Controls
Notes: SG page vi
Instruction
The Lifting Operations Fatal Risk is defined as exposure to loss of control of a load suspended by a crane (fixed or mobile), hoist, forklift, boom or other lifting equipment
Discuss the Critical Controls
  Barriers and Segregation
  Lifting Execution
  Mechanical Integrity of Lifting Equipment

## Slide 16
Uncontrolled Release of Energy
SG vii
Stored energy from pressure
Items under tension or compression
Critical Controls
Notes: SG page vii
Instruction
The Uncontrolled Release of Energy Fatal Risk is defined as exposure to stored energy from pressure (e.g., pneumatic systems, hydraulic systems, steam, tires, etc.); Items under tension or compression (e.g., mooring lines, springs, counterweights, etc.)
Discuss the Critical Controls
  Energy Isolation/LOTOTO
  Guards, Barriers, and Barricades
  Hose Coupling Lock System
  Pipe Management
  Piping Hoses and Equipment Mechanical Integrity
  Relief Valves
  Tensioned Lines Management
  Tire Management

## Slide 17
Vehicle Impact on Person
SG vii
Person struck by vehicle/mobile equipment
Critical Controls
Notes: SG page vii
Instruction
The Vehicle Impact on Person Fatal Risk is defined as person struck by vehicle/mobile equipment.
Discuss the Critical Controls
  Fundamentally Stable Parking
  Positive Communication System
  Segregation
  Signage and Demarcation
  Vehicle Preoperational Inspection

## Slide 18
Module 1: Introduction
Notes: SG page 3
Instruction
Review learning objectives for the module
Upon completion of this module, students will be able to
  Describe the history and purpose behind FCX-HS12

## Slide 19
Safe Production
“Safe Production is an integral part of our culture and our top priority.”
Red Conger, President
Freeport-McMoRan Inc. Americas
High-Density Polyethylene Pipe
Introduction Video
Notes: SG page N/A
Instruction
Safe Production is the driving force behind standardizing HDPE Pipe Handling
HDPE stands for High-Density Polyethylene Pipe
The video introduces HDPE, its characteristics, its inherent hazards, and safe handling techniques

## Slide 20
HDPE Pipe Handling
Notes: SG page N/A
Instruction
Click on the link below to play the video- check the volume ahead of time
https://web.microsoftstream.com/video/60697858-3637-4a11-842c-77653e599429

## Slide 21
HDPE Pipe Characteristics
SG 5
Valuable Asset
  Durability
  Flexibility
  Thick walls
  Resilience
Hazards
  Heavy
  Stores Energy
Notes: SG page 5
Instruction
Many in the mining industry commonly use High-Density Polyethylene Pipe
It is a valuable asset due to its:
  Durability and flexibility
  Thick walls and resilience to most any material
These same characteristics can make it hazardous due to its:
  Ability to store and release energy quickly
  Doubled with the heavy weight
  Serious injuries or fatalities could occur due to mishandling of the HDPE Pipe

## Slide 22
Fatality Prevention
SG 5
Policy developed
Pipe Safety Steering Team (PSST)
Notes: SG page 5
Instruction
Policy was developed to prevent incidents with HDPE Pipe
  Focus on this quote from SG page 5: “The safety and health of all Freeport-McMoRan Inc. (“FCX”) employees is of the highest priority and a core value of the company. Our objective is zero workplace injuries and occupational illnesses. Production and costs are critical to the well-being of the company, but these considerations must never take precedence over safety, employee health or protection of the environment.”
PSST developed to address incidents occurred in relation to HDPE Pipe
  Developed a policy of best practices to work safely with HDPE Pipe
  All sites who handle HDPE Pipe must follow policy (FCX-HS12)

## Slide 23
Policy Scope
SG 5
Who must attend HDPE Pipe handling training?
Which commonly used pipe are not included in the policy?
Notes: SG page 5
Instruction
All employees and contractors who handle or participate in the handling of HDPE Pipe must attend the training course
Drip line or corrugated pipe does not present the same hazard as HDPE Pipe

## Slide 24
Directions
From the Learn from Others presented, answer the questions in your student guide.
Discuss and share your thoughts about what could have been done differently.
Just the Facts
Activity 2
SG 7
Notes: SG page 7
Time
Approximately 10 minutes
Materials
Student Guide
Pens/Pencils
Purpose
This activity gives students the opportunity to learn about one of the incidents that prompted improved coordinated guidelines, training, and policy.
Instruction
Divide the class into three groups.
Have each group read/discuss and be ready to summarize one of the next three “Learn From Others.”
Have students take notes on page 7 of SG.
Group 1- page 8 (included here on page 25)
Group 2- page 9 (included here on page 26)
Group 3- page 10 (included here on page 27)
Animation- During their summaries, when you click, the picture will enlarge for easier visibility.
[Note: Include directions that recognize varying class sizes by doing one of the following
Provide an activity where class size does not matter
Incorporate suggestions to alter the given activity for larger and smaller than defined class sizes
Provide alternate activity for larger and smaller than defined class sizes]

## Slide 25
Learn from Others
SG 8
Notes: SG page 8
Instruction
Have a student read on page 8 of the SG
Discuss
Click to show an enlarged portion of the picture to show details of the positioning

## Slide 26
Learn from Others
SG 9
Notes: SG page 9
Instruction
Have a student read the first on page 9 of the SG
Discuss
Click to show 2 more pictures to illustrate the scene

## Slide 27
Learn from Others
SG 9
Notes: SG page 9
Instruction
Have a student read the second one found on page 10 of the SG
Discuss
Click the picture to enlarge for easier visibility

## Slide 28
Quiz
Directions
Complete the quiz in the Student Guide (p. 12)
Discuss the answers as a class
Module 1 Quiz
SG 12
Notes: SG page 12
Instruction
Give students time to write answers to the quiz questions in the SG
Review the answers as a class using the slides

## Slide 29
Module 1 Quiz
SG 12
What does HDPE stand for?
  High Density Polyethylene
  High Density Plastic Energy
  High Density Polycarbonate Emergence
Notes: SG page 12
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, SG page 5

## Slide 30
Module 1 Quiz
SG 12
What properties make handling HDPE Pipe so hazardous? (circle all that apply)
  Heavy
  Elasticity
  Easy to install
  Impervious to many chemicals and solutions
Notes: SG page 12
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, b, d, SG page 5

## Slide 31
Module 1 Quiz
SG 12
What should be done if you feel unsafe, or if a co-worker is in danger?
  Stop the job and abandon the task
  Stop the job and receive clarification
  Walk away from the task and have someone else complete it
  Wait until the task is complete and discuss the situation with your supervisor.
Notes: SG page 12
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
b, SG page 6

## Slide 32
Debrief
What are some key concepts learned in this module?
What do you need to understand better?
What information surprised you?
Notes: SG N/A
Instruction
Discuss questions on slide

## Slide 33
Module 2: Risk Management
Notes: SG page 15
Instruction
Review learning objectives for the module
Upon completion of this module, students will be able to
  Describe the purpose and process for hazard recognition before performing tasks related to working with HDPE Pipe
  Identify the personnel who will be associated with the task, as well as their roles and responsibilities, to ensure the task is being performed safely and all involved abide by policy

## Slide 34
Hazard Assessment
SG 17-18
Risk Registers
Workplace Examinations
Job Safety Analysis
Notes: SG pages 17-18
Instruction
Ask the following questions to begin discussion:
What happens when a crew does not complete an adequate hazard assessment at their work site?
What happens when they do not think through the job steps and look for potential hazards?
What happens when they do not have proper controls in place, or if they skip steps?
  Hazards in the workplace are the things that could hurt you, or lead to incidents with serious and potentially fatal consequences
  Overlooking hazards in the workplace can have catastrophic, yet completely preventable, outcomes
Discuss the following types of Hazard Assessments:
  Risk Registers
    Tasks involving HDPE Pipe handling will be listed on divisional risk registers at each site
    Evaluation to reduce or eliminate risk will be completed according to safety policies
    Listed on Risk Registers will be:
      Analysis of the risks involved
      Controls that must be in place in order to mitigate risks
        Bringing the hazard level down to an acceptable level
        Placed within the policy as a directive from the company
        If the steps and actions are completed as described, the employees handling the HDPE Pipe have the greatest probability of completing their job safely
  Workplace Examinations
    Before any work commences
      Critical to look around and assess all areas connected to the job, from staging to installation
      Guide workers as they take a critical review of the physical space in which they will work
      Form has room for documentation of any hazardous situation within the physical space, such as:
        Areas that need cleanup
        Situations that could create a hazardous situation, such as:
          Equipment
          Guarding
          Walkways that need to be fixed
          Within the context of jobs including HDPE Pipe handling, looking at physical locations and assessing the ground and roadways
  Job Safety Analysis
    Performing a job considered high risk and non-routine
      Plan well
      Anticipate any risks they may face.
    Tool to assist the workers as they:
      Think through their job
      Discuss the steps
      Look for the potential hazards they could encounter with each step
    When a potential risk is identified, they must:
      Decide on the most effective critical control to keep the risk from creating an unsafe working environment
    The JSA form gives an opportunity to record these steps, as well as the controls chosen to mitigate the risks
    After the work has been completed, there is a section for the workers to write:
      Notes and document any ideas
      Consequences
      Thoughts
      Descriptions
      Anything that will help the next team of workers to have the necessary information

## Slide 35
Hierarchy of Controls
SG 18
Notes: SG page 18
Instruction
Ask “What do you remember about the Hierarchy of Controls?”
Review each level below:
Elimination: most effective, as it completely eliminates the hazard
Substitution: is there something that can be used in place of the item/process so as to keep the employees safer?
Engineering: Is there anything we can design/build that will keep us away from the hazard?
Administrative: Rules, policies, signage (depends on employees to read and follow, so not as effective)
PPE: Personal Protective Equipment- what we put on to keep us “safe” from the hazards. This is the least effective, as it is completely dependent on human behavior. Does the person choose the correct equipment to protect them from the specific hazards, and then did they actually put it on , and put it on correctly?

## Slide 36
Be On the Lookout
SG 19
Notes: SG page 19
Instruction
Click on the following link to play video
https://web.microsoftstream.com/video/26fd9ad0-1776-490d-ad2d-2a7285c9d204
Have a student read (or you can read) the scenario on page 19 of the student guide
Discuss the following questions:
  What happened?
  Could this have been prevented?
  How?

## Slide 37
Planning
SG 20
Per FCX-HS12 requires four main considerations:
Safe work procedures
Equipment manufacturer’s procedures
Training
Repair
Notes: SG page 20
Instruction
As per FCX-HS12, planning for work which involves HDPE Pipe handling requires four main considerations:
Establish safe work procedures and identify and remove hazards before beginning a task
Follow the equipment manufacturer's procedures for the work being performed to ensure all hazards have been addressed
Train persons to recognize the hazards associated with performing a task
Repair all equipment found to be damaged prior to performing the work, or take the equipment out of service and replace it with another piece of equipment appropriate for the task
A few key concepts and definitions need to be clearly defined and taken into account regarding the necessary people and appropriate circumstances needed when planning a job that includes HDPE Pipe handling

## Slide 38
Team
SG 20-21
The following people must be included in planning a job:
A qualified individual
Project lead
Supervisor
Project Managers
Notes: SG pages 20-21
Instruction
A Qualified Individual is an employee is:
  Familiar with the operation and safety hazards of the task through training and experience
  Qualified using the applicable skills assessments
The Project Lead is:
  Intimately familiar with the task
  Could be a supervisor, engineer leading the project, or other Qualified Individual
Supervisors at each site will be responsible to ensure that practices are being followed
Project Managers will:
  Audit work practices of contractors
  Ensure compliance with site HDPE Pipe procedures and this policy

## Slide 39
Team
SG 20-21
Engineer
Pipe pulling escorts
Safety watch
Spotter
Notes: SG pages 20-21
Instruction
An engineer is:
  “A person trained in or follows as a profession a branch of engineering”
  Someone who works with and is knowledgeable of the characteristics and hazards associated with HDPE Pipe
Pipe Pulling Escorts:
  A Lead Escort and Trail Escort are required for:
    Pulling pipe in addition to the pulling equipment when there is potential for interaction with other traffic
  All equipment involved with this task must be equipped with a:
    Flashing blue light
    Blue light easily visible during daylight hours
  Trail Escort must maintain a distance of at least 50 feet behind the pipe that is being pulled
  Lead Escort and Trail Escort used during a pipe pull must not have any other assignments or responsibilities
Safety Watch is a:
  Qualified Individual set to monitor a job involving HDPE Pipe
  A person who must remain on the job at all times and have no other job assignments or responsibilities
  If this person must leave the area:
    There must be positive relief by another Qualified Individual
  Requirement determined by the hazards associated with specific tasks, including specific policy requirements for example:
    When substantial barriers are used
    Must be well versed in the equipment being used
    Needs to know when to “stop the job” and reassess the situation
A Spotter is a person:
  Assigned to assist or direct flow of work for someone performing a task, such as unloading or moving pipe
  Who must be cautious and stay out of the line of fire of the pipe while staying in the line of sight for the equipment operator

## Slide 40
Circumstances and Requirements
SG 22
Safety reminders:
Block material
Position
Monitor
Notes: SG page 22
Instruction
Listed below are several safety reminders while performing work with HDPE Pipe:
Block material against motion to assure energy cannot be released
Do not place yourself in a position that will expose you to hazards
Monitor personnel routinely to determine safe work procedures are followed

## Slide 41
Circumstances and Requirements
SG 22
When planning consider the following:
Management of Change (MOC)
Load/Move
Notes: SG page 22
Instruction
Understand and consider the following circumstances and requirements when planning any job that includes HDPE Pipe handling:
  Management of Change (MOC)
    Corporate initiative
    Required by all Freeport-McMoRan properties since company is ISO 14001 certified
    Must be submitted and completed before attempting jobs that create any addition or change to the company properties
    Gives Health and Safety Department and Environmental Department opportunity to evaluate changes for potential impacts on the following:
      Safety
      Environmental
      Production
      Quality
    Health and Safety Department and Environmental Department need time to determine and must be done before work begins if:
      Specific samples need to be taken
      Other permits need to be obtained
      Land needs to be surveyed
      Endangered plants and animal studies need to be performed
    According to FCX-HS12, each site’s MOC system must be considered when planning a job that requires working with HDPE Pipe.
  Load/Move
    Information for each piece of equipment:
      Must be gathered
      Must be available to the planning team
      Will be used to assist decisions
      Will include site-specific equipment

## Slide 42
Circumstances and Requirements
SG 22-23
Engineering Review
Pushing Pipe
Positioning Pipe
Notes: SG pages 22-23
Instruction
Engineering Review
  For specific tasks where the policy covers the general safe practices, but not details of the engineering
  The Engineering Review may be used for the following situations:
    Pulling pipe of any diameter that is longer than 400 feet
    Pulling pipe up or down grades greater than 25%
    Pushing pipe
    Tasks involving dual-walled or dual-contained pipe
    Fusing pipe that is not consistent or without manufacturer specifications or ASTM standards
    Pulling or fusing pipe 42 inches in diameter and greater
  While the engineering review is being completed, all manufacturer and company-defined safety standards must be utilized
  The details of the engineering review must be attached to the request, or be readily available if an attachment is not practical
Pushing Pipe
  Pulling will be used over pushing wherever possible
  Pushing is very dangerous, it is extremely difficult to control the stored energy created by this activity
  An Engineering Review is required for pushing pipe
  If there is no alternative to pushing pipe, this job can only be performed by a Qualified Individual once the job has received the appropriate planning and approvals
  More specific information regarding pushing pipe will be covered in Module 4
Positioning Pipe
  Click on the picture to show a video about Positioning Pipe
  Final Positioning can be as simple as nudging the pipe into place
  Final positioning can still be dangerous because the pipe may build up a small amount of stored energy or move unexpectedly
  Those completing this task must still be aware of the hazards and stay out of the line of fire
  Potential stored energy may still create risk to the employee, so careful planning should take place before commencing Final Positioning

## Slide 43
Circumstances and Requirements
SG 24
Substantial Barriers
Pipe Guide
Dual-Walled Pipe
Notes: SG page 24
Instruction
Substantial Barriers
  Object used for controlling the energy in the pipe to protect personnel must be within the 50-foot safe zone
  Examples of barriers:
    Dirt berms
    Concrete barriers
    Properly placed equipment
  Requirements for the use of a Substantial Barrier are determined by:
    Hazards associated with specific tasks
    Specific policy requirements
Pipe Guide
  Equipment or material used to maintain control of the energy of the pipe while being moved
  Must not present a hazard to the operator or equipment.
  Equipment used must be appropriate for the size and potential energy of the pipe
  Equipment used can be within the 50-foot safe zone
  Requirements for the use are determined by the hazards associated with specific tasks, including specific policy requirements
Dual-Walled Pipe (Dual-contained pipe)
  May require different rigging or equipment or both specific to the pipe and task
  Engineering Review is required
  Applies specifically to pipe manufactured as dual-walled or dual-contained pipe
  Does not apply to sleeved pipeline assembled on site

## Slide 44
Circumstances and Requirements
SG 24-25
Preventative Maintenance
Variance Request
Notes: SG pages 24-25
Instruction
Preventative Maintenance
  Establish process for inspection of pipes using each site’s existing PM process
  Perform inspections for the following issues:
    Sagging
    Ground erosion
    Condition of equipment for example pulling heads, slings, shackles, and swivels
    Components will be described in greater detail and available to handle during the hands-on portion of Module 4
Variance Request
  Process outlined within FCX-HS01 “Policy Administration Requirement” allows for justifiable variances from the policies
  When a Health and Safety Policy cannot be met, a Variance Request must be completed, reviewed and approved
  When HDPE Pipe work falls outside of the scope of FCX-HS12 or the “Policy Administration Requirements”, FCX-HS01 states a “Short-Term Variance” is required in “Situations that are temporary in nature where work is in progress and the specific conditions of the work area or other parameters may not allow for full compliance with a policy
    The following are situations a Short-Term Variance are used:
      One-time events
      Emergency situations
      Work in regions where equipment to comply is not immediately available
      Site conditions which do not allow for compliance
      Where alterations to the facility would be required
  Short-term variances should be:
    Restricted to non-routine work activities where unanticipated conditions make compliance infeasible or more hazardous
    Evaluated as part of continuous improvement of safe work practices

## Slide 45
Directions
Your instructor will divide you into groups
Follow the instructions in each box below.
Tell Me That Again
Activity 3
SG 26
Notes: SG page 26
Time
Approximately 10 minutes
Materials
Student Guide
Pen/Pencil
Purpose
This activity gives students the opportunity to review and summarize from the policy several key definitions.
Instruction
Divide class in half (thirds if you have enough).
First group will read pages 20-21 and be ready to discuss the team players, along with a 10 second description of each.
Second group will read pages 22-25 and be ready to discuss the circumstances and requirements that must be part of the planning process (10 second summary).
If your class is large enough to divide into thirds, you can have the last group review and be ready to explain pages 17-18. If not, go over this quickly as a review with everyone.
The groups are welcome to divide and conquer their information or work together as needed.
[Note: Include directions that recognize varying class sizes by doing one of the following
Provide an activity where class size does not matter
Incorporate suggestions to alter the given activity for larger and smaller than anticipated class sizes
Provide alternate activity for larger and smaller than anticipated class sizes]

## Slide 46
Quiz
Directions
Complete the quiz in the Student Guide (pp. 27-28)
Discuss the answers as a class
Module 2 Quiz
SG 27-28
Notes: SG pages 27-28
Instruction
Give students time to write answers to the quiz questions in the SG
Review the answers as a class using the slides

## Slide 47
Module 2 Quiz
SG 27
The following are Hazard Recognition tools you can use when planning jobs that include HDPE Pipe handling (Circle all that apply):
  Risk Register
  Workplace Exams
  Job Safety Analysis
  HDPE Safety Reminders
Notes: SG page 27
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, b, c, SG pages 17-18

## Slide 48
Module 2 Quiz
SG 27
Match these terms with their definitions:
Qualified Individual | ___ Assigned to assist or direct flow of work for someone performing a task, such as unloading or moving pipe.
Project Lead | ___ “A person who is trained in or follows as a profession a branch of engineering” and someone who works with and is knowledgeable of the characteristics and hazards associated with HDPE Pipe.
Supervisor | ___ Intimately familiar with the operation and safety hazards of the task.
Project Manager | ___ Required for pulling pipe in addition to the Pulling Equipment when there is potential for interaction with other traffic.
Engineer | ___ Will audit work practices of contractors that perform HDPE Pipe tasks to ensure compliance with site HDPE Pipe procedures and this policy.
Pipe Pulling Escort | ___ Qualified Individual who is set to monitor a job including HDPE Pipe.
Safety Watch | ___ An employee that through training and experience is familiar with the operation and safety hazards of the task.
Spotter | ___ Responsible to ensure that practices are being followed.
Notes: SG page 27
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
h, e, b, f, d, g, a, d, SG pages 20-21

## Slide 49
Module 2 Quiz
SG 28
What are the three main considerations when planning for work with HDPE Pipe handling? (Circle all that apply)
  Repair broken or damaged equipment immediately
  Train person to recognize the hazards associated with performing a task
  Establish safe work procedures and identify and remove hazards before beginning a task
  Assign a team member to complete the hazard recognition forms, such as the JSA and Workplace Exam
Notes: SG page 28
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, b, c, SG page 20

## Slide 50
Module 2 Quiz
SG 28
Label these drawings “Pushing” or “Positioning”
a. __________________________
b. __________________________
c. ________________________
Notes: SG page 28
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
Pushing, Positioning, Pushing, SG page 23

## Slide 51
Debrief
What are some key concepts learned in this module?
What do you need to understand better?
What information surprised you?
Notes: SG N/A
Instruction
Discuss questions on slide

## Slide 52
Module 3: Pipe Handling
Notes: SG page 31
Instruction
Review learning objectives for the module
Upon completion of this module, students will be able to
  Describe safe practices and requirements of FCX-HS12 regarding receiving, loading, unloading and storage of HDPE Pipe on FCX properties
  Identify when to use the Receiving/Loading/Unloading Checklist, and describe how to fill out this form correctly
  Identify the difference between a properly loaded shipment of HDPE Pipe and one that does not comply with the company’s shipping standards
  Describe the procedure in place to report loads that do not meet company standards
  Describe how to safely store HDPE Pipe according to policy requirements

## Slide 53
HDPE Pipe Loading & Unloading
Notes: SG page N/A
Instruction
Click on the link below to play video
https://web.microsoftstream.com/video/4fb1e8b2-5dd1-4707-983c-7ee35273c380

## Slide 54
Receiving from External Source
SG 33
Safe practices must be followed when:
  Receiving
  Storing
Notes: SG page 33
Instruction
HDPE Pipe is shipped to properties by vendors
Safe practices must always be adhered to when receiving the pipe:
  Arrival of the shipping truck at the unloading site must be coordinated
  Trucks will not be unloaded until checklist is complete
  If load not compliant with Shipping Requirements the following is required prior to unloading:
      Additional evaluation
      Superintendent approval
  Includes a reporting system for communicating improper loads to Global Supply Chain (GSC)
  Requirements found on the FCX-DOHS SharePoint Site
  For further questions, contact your Supervisor or Project Lead
Safe practices must always be adhered to when storing the pipe:
  Without engineered controls:
    Stored no more than two pipes high for 10 inch diameter and larger
    Stored no more than 2 feet high for pipe smaller than 10 inch diameter
  HDPE Pipe can be stored higher with engineered controls to prevent the stack from collapsing

## Slide 55
Shipping
SG 33
Variance Request
Follow company shipping requirements
Notes: SG page 33
Instruction
Variance Request is required for pipe being shipped off-site
HDPE Pipe must be shipped according to the company shipping requirements according to FCX-HS12
  Located in the HDPE Pipe Shipping Requirements document
  Found on the FCX-DOHS SharePoint Site

## Slide 56
Be On the Lookout
SG 34-35
Safety Success (September 27, 2013)
Notes: SG pages 34-35
Instruction
Divide the class in half-one half will discuss the Be On the Lookout while the other will discuss the Learn From Others
  Students should pair up and read their assigned section
  Students should take notes about the situation in preparation for the discussion
  After partner discussion, have each group summarize the details
  As a whole class, discuss the similarities and differences between the two

## Slide 57
Learn from Others
SG 35
MSHA Fatality Overview (MAI-2016-01)
Notes: SG page 35
Instruction
Divide the class in half-one half will discuss the Be On the Lookout while the other will discuss the Learn From Others
  Students should pair up and read their assigned section
  Students should take notes about the situation in preparation for the discussion
  After partner discussion, have each group summarize the details
  As a whole class, discuss the similarities and differences between the two

## Slide 58
On-Site Transfers and Movement
SG 36
HDPE Pipe Receiving/Loading/Unloading Checklist
Site trailers
Notes: SG page 36
Instruction
On-Site Transfers require the following prior to beginning a task:
  HDPE Pipe Receiving/Loading/Unloading Checklist needs to be completed
  Adhere to established procedure for ensuring the checklist is completed
Site trailers used for on-site transfers of HDPE Pipe must be:
  Equipped with engineered stints, or
  Other engineered means of securing the load

## Slide 59
On-Site Transfers and Movement
SG 36
Equipment
Safe Zone
Notes: SG page 36
Instruction
Equipment
  There are several requirements to consider when planning to move HDPE Pipe from one location to another on the site
  The requirements are listed below:
    The site must ensure equipment has been evaluated for adequate lifting capacity, and the equipment operator is aware of the limitations of the equipment
    Equipment operators must have documented training for the equipment used in the loading/unloading process
    Documented rigging task training is required for employees loading/unloading pipe using a mobile crane
Safe Zone
  A 50-foot Safe Zone around the truck must be:
    Established
    Marked with a Safety Watch in place to keep ground personnel out of the loading/unloading zone any time the load is not secure
    Truck driver must remain with the Safety Watch any time the load is not secure
  Safety Watch must:
    Be a qualified individual who is experienced and knowledgeable in the job being completed
    Remain on the job at all times and have no other job assignments
  A Substantial Barrier must be in place for personnel to enter the Safe Zone when:
    Load is not secured
    Load is being strapped or unstrapped
    Example: a loader with forks to block the load when unstrapping

## Slide 60
On-Site Transfers and Movement
SG 37
Hazard Boundary
Pipe Coils
Notes: SG page 37
Instruction
Hazard Boundary
  Area which task hazards exist must be reviewed and defined
    Must include the need for any boundary markings
    Anyone who is inside this area will review and sign the completed HDPE Pipe Handling Permit
    Required to ensure all personnel are aware of the hazards
    Additional review(s) may be needed if there is more than one task taking place on the same pipeline
Pipe Coils
  Specific procedures will be developed for any diameter and length
  HDPE Pipe Handling Permit will be issued prior to starting work
  This procedure must include:
    Where the pipe will be staged after it is unrolled
    Controls used to maintain a secure area
  The process of unrolling HDPE Pipe coils up to the staging area is not:
    Considered pulling pipe
    Restricted to the 400 foot maximum length
  After the unrolled pipe has been staged, the pipe is subject to the pipe pulling requirements
  An engineered device for controlling the stored energy in the coil (such as a Line Tamer) must be used when unrolling coils
  No restrictions on the length of pipe in a coil to be unrolled

## Slide 61
Learn from Others
SG 38-39
Notes: SG pages 38-39
Instruction
Have the students read/skim through this Learn from Others individually
As a class:
  Summarize the scenario
  Actions taken
  Key findings

## Slide 62
Specific Forms
SG 40
HDPE Pipe Handling Permit
HDPE Pipe Handling Engineering Review
Receiving/Loading/Unloading checklist
Notes: SG page 40
Instruction
HDPE Pipe Handling Permit
  Main form needed for most situations concerning HDPE Pipe handling
  Filling out this form completely is Step #1 when planning out the job
HDPE Pipe Handling Engineering Review
  Complete and submit this form along with the Permit in order to develop a plan to accomplish a task not specifically covered in the Policy
Receiving/Loading/Unloading checklist
  Must be completed prior to the loading/unloading activity and when receiving HDPE
These documents and all HDPE Pipe Handling permits, policy, and technical supplements can be found on the DOHS SharePoint under H&S Policies, HDPE Pipe Handling

## Slide 63
HDPE Pipe Handling Permit
When to complete the Permit
How long is it good
Who is it reviewed by
Who signs the form
Notes: SG page 40
Instruction
Completed for
  Any work with HDPE Pipe that is 2 inches in diameter or larger and longer than 50 feet where the pipe will be pulled, installed, and/or repaired
  Unrolling HDPE Pipe coils, regardless of diameter and length
Good for the task duration as long as conditions do not change
  Examples include weather, equipment, pipe size, terrain, slope, project lead, etc.
Permit must be reviewed by all employees associated with the task each time prior to work beginning
Each employee must print, sign, and date the bottom of the permit in the designated area (or the reverse side of the permit) after the permit is reviewed

## Slide 64
HDPE Pipe Handling Permit, Page 1
SG 41
Notes: SG page 41
Instruction
This is page one of the HDPE Pipe Handling Permit
We will discuss the details of the form in the upcoming slides

## Slide 65
HDPE Pipe Handling Permit, Page 2
SG 42
Notes: SG page 42
Instruction
This is page two of the HDPE Pipe Handling Permit
We will discuss the details of the form in the upcoming slides

## Slide 66
Think Safely
SG 43
Notes: SG page 43
Instruction
Discuss the information in the red boxes

## Slide 67
Initial Information
SG 43
Notes: SG page 43
Instruction
Discuss the information in the red boxes

## Slide 68
Description
SG 44
Notes: SG page 44
Instruction
Discuss the information in the red boxes

## Slide 69
Section 1: General Hazard Analysis
SG 44
Notes: SG page 44
Instruction
Pre-Job Analysis portion of the permit
  Section 1 covers questions related to a General Hazard Analysis
    Each line item must be reviewed and the appropriate box checked
    Advisable to enter additional information on some of the line items to document specific details
Discuss the information in the red boxes

## Slide 70
Section 1: General Hazard Analysis cont’d
SG 45
Notes: SG page 45
Instruction
Discuss the information in the red boxes

## Slide 71
Section 1: General Hazard Analysis cont’d
SG 45
Notes: SG page 45
Instruction
Discuss the information in the red boxes

## Slide 72
Section 2: Pulling Analysis
SG 46
Notes: SG page 46
Instruction
Analyzing the pulling of pipe
If the task you are performing does not require pipe pulling, you may mark this section as NA
Discuss the information in the red boxes

## Slide 73
Section 3: Fusing/Installation/Repair
SG 46
Notes: SG page 46
Instruction
If the task you are performing does not require pipe fusing, installation or repair, you may mark this section as NA
Discuss the information in the red boxes

## Slide 74
Section 3: Fusing/Installation/Repair cont’d
SG 47
Notes: SG page 47
Instruction
Discuss the information in the red boxes

## Slide 75
Section 4: Energy Resource Review
SG 47
Notes: SG page 47
Instruction
Discuss the information in the red boxes

## Slide 76
Section 4: Energy Resource Review cont’d
SG 47
Notes: SG page 47
Instruction
Discuss the information in the red boxes

## Slide 77
Section 4: Energy Resource Review cont’d
SG 48
Notes: SG page 48
Instruction
Discuss the information in the red boxes

## Slide 78
Section 5: Significant Hazard Analysis
SG 48
Notes: SG page 48
Instruction
Discuss the information in the red box

## Slide 79
Section 5: Significant Hazard Analysis cont’d
SG 48
Notes: SG page 48
Instruction
Discuss the information in the red box

## Slide 80
Section 5: Significant Hazard Analysis cont’d
SG 49
Notes: SG page 49
Instruction
Discuss the information in the red box

## Slide 81
Qualified Individual
SG 49
Notes: SG page 49
Instruction
Discuss the information in the red boxes

## Slide 82
HDPE Pipe Handling Engineering Review
SG 50
Notes: SG page 50
Instruction
Depending on the task being performed, an Engineering Review may be required
  For specific tasks where the policy covers the general safe practices, but does not cover the details of the engineering
  May be used for the following situations:
    Pulling pipe of any diameter that is longer than 400-feet
    Pulling pipe up or down grades greater than 25%
    Pushing pipe
    Tasks involving dual-walled or dual-contained pipe
    Fusing pipe that is not consistent or without manufacturer specifications or ASTM standards
    Pulling or fusing pipe 42 inch in diameter or greater
  All manufacturer and company-defined safety standards must be used
  Details of the engineering review must be:
    Attached to the request or be readily available if an attachment is not practical
    Retained according to the FCX Records Retention Policy

## Slide 83
Initial Information
SG 51
Notes: SG page 51
Instruction
Discuss the information in the red boxes

## Slide 84
Description·Review·Controls
SG 52
Notes: SG page 52
Instruction
Discuss the information in the red boxes

## Slide 85
Approvals
SG 53
Notes: SG page 53
Instruction
Discuss the information in the red boxes

## Slide 86
HDPE Pipe Receiving/Loading/Unloading Checklist
SG 54
Notes: SG page 54
Instruction
An HDPE Pipe Receiving/Loading/Unloading Checklist must be:
  Completed prior to receiving, loading, or unloading HDPE Pipe
  Reviewed by all employees associated with the task
  Signed by all personnel involved with the task in the appropriate locations
HDPE Pipe must be shipped according to company shipping requirements
  Located in the HDPE Pipe Shipping Requirements document
Arriving loads not compliant with the HDPE Pipe Shipping Standards require the following:
  Additional evaluation
  Superintendent approval prior to unloading as indicated on the checklist
  A reporting system for communicating improper loads to GSC

## Slide 87
Initial Information
SG 55
Notes: SG page 55
Instruction
Discuss the information in the red boxes

## Slide 88
Part 1 – HDPE Pipe Load Checklist
SG 55
Notes: SG page 55
Instruction
Discuss the information in the red boxes

## Slide 89
Part 2 – HDPE Pipe Load Checklist
SG 56
Notes: SG page 56
Instruction
Discuss the information in the red boxes

## Slide 90
Part 2 – HDPE Pipe Load Checklist cont’d
SG 57
Notes: SG page 57
Instruction
Discuss the information in the red boxes

## Slide 91
Part 2 – HDPE Pipe Load Checklist cont’d
SG 57
Notes: SG page 57
Instruction
Discuss the information in the red boxes

## Slide 92
Part 3 – HDPE Pipe Load Checklist
SG 58
Notes: SG page 58
Instruction
Discuss the information in the red boxes

## Slide 93
Part 3 – HDPE Pipe Load Checklist cont’d
SG 58
Notes: SG page 58
Instruction
Discuss the information in the red boxes

## Slide 94
Part 3 – HDPE Pipe Load Checklist cont’d
SG 59
Notes: SG page 59
Instruction
Discuss the information in the red boxes

## Slide 95
Part 3 – HDPE Pipe Load Checklist cont’d
SG 60
Notes: SG page 60
Instruction
Discuss the information in the red boxes

## Slide 96
Part 3 – HDPE Pipe Load Checklist cont’d
SG 61
Notes: SG page 61
Instruction
Discuss the information in the red boxes

## Slide 97
Part 3 – HDPE Pipe Load Checklist cont’d
SG 62
Notes: SG page 62
Instruction
Discuss the information in the red boxes

## Slide 98
Directions
Complete this activity by circling the correct section within the Pipe Handling Permit you would find these questions.
Circle Up
Activity 4
SG 63
Notes: SG page 63
Time
Approximately 10 minutes
Materials
SG page 63
Pen/Pencil
Purpose
This activity gives students the opportunity to individually process the materials just discussed. They will be able to review the sections of the Pipe Handling Permit.
Instruction
This activity is completed individually.
Complete this activity by circling the correct location within the Pipe Handling Permit that you would find these questions.
Take time to go over the answers (slide 115-116) with them before going into the module quiz.
Answers
5
4
5
2
2
1
4
3
2
Note: Include directions that recognize varying class sizes by doing one of the following
Provide an activity where class size does not matter
Incorporate suggestions to alter the given activity for larger and smaller than anticipated class sizes
Provide alternate activity for larger and smaller than anticipated class sizes]

## Slide 99
Quiz
Directions
Complete the quiz in the Student Guide (p. 64)
Discuss the answers as a class
Module 3 Quiz
SG 64
Notes: SG page 64
Instruction
Give students time to write answers to the quiz questions in the SG
Review the answers as a class using the slides

## Slide 100
Module 3 Quiz
SG 64
Only portions of the Pipe Handling Permit, which apply to the task being performed, need to be completed.
  True
  False
Notes: SG page 64
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, SG page 40

## Slide 101
Module 3 Quiz
SG 64
When must the Pipe Handling Engineering Review be used? (Circle all that apply)
  Every time the Permit is used
  When pushing the pipe is the only alternative
  When pipes are dual-contained or dual-walled
  Pulling or fusing pipe ≥ 42 inches in diameter
  When the pipe handling job has scenarios not covered in the Policy
Notes: SG page 64
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
b, c, d, SG page 50

## Slide 102
Module 3 Quiz
SG 64
When must a HDPE Pipe handling permit be completed? (Circle all that apply)
  When unrolling HDPE Pipe coils
  When HDPE Pipe is being loaded and unloaded
  Any time you are working with HDPE Pipe regardless of length
  When performing any work with HDPE Pipe 2 inches in diameter or larger and longer than 50 feet
Notes: SG page 64
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, d, SG page 40

## Slide 103
Debrief
What are some key concepts learned in this module?
What do you need to understand better?
What information surprised you?
Notes: SG N/A
Instruction
Discuss questions on slide

## Slide 104
Module 4: Rigging
Notes: SG page 67
Instruction
Review learning objectives for the module
Upon completion of this module, students will be able to
  Describe the proper procedures required to safely pull various sizes and lengths of HDPE Pipe according to policy requirements
  Identify the proper equipment required for the task
  Identify appropriate forms for the tasks that will be performed and describe how to fill out these forms correctly

## Slide 105
Pulling/Moving HDPE Pipe
Notes: SG page N/A
Instruction
Click on the link to play video
https://web.microsoftstream.com/video/e7a8465a-2e73-4683-9069-31d173717d6d

## Slide 106
Pulling Pipe Versus Pushing Pipe
SG 69
Ways to move pipe from one location to another:
  Pushing
  Pulling
  Positioning
Notes: SG page 69
Instruction
Ways to move the pipe from one location to another on a property
  Pulling Pipe
  Pushing Pipe
  Final Positioning of Pipe
Each have their specific hazards associated due to:
  Control, or
  Lack of control, of the stored energy that can be created during the process of moving

## Slide 107
Pulling Pipe Versus Pushing Pipe
SG 69
Pulling
Notes: SG page 69
Instruction
Requires connection to a large piece of equipment that can handle the amount of weight associated with pulling the pipe to where it will be needed to complete a job
Specific planning is needed to determine the appropriate rigging assemblies that will need to be used
Technical supplements are provided in FCX-HS12 to guide this planning process

## Slide 108
Pulling Pipe Versus Pushing Pipe
SG 69-70
Pushing
Notes: SG pages 69-70
Instruction
Requires the appropriate equipment to move the pipe from behind or alongside the pipe, moving it a significant distance to the desired location
According to FCX-HS12, pulling will be used over pushing wherever possible due to the additional hazards created when pushing
Pushing pipe requires an Engineering Review before it can be performed

## Slide 109
Pulling Pipe Versus Pushing Pipe
SG 70
Positioning, or Final Positioning
Notes: SG page 70
Instruction
Different than pushing or pulling
Can be as simple as using a piece of equipment to nudge the pipe into the desired position as needed for the job
Potential stored energy could still create a risk to the employee, so careful planning should still take place before commencing positioning, or Final Positioning

## Slide 110
Learn from Others
SG 71-72
Notes: SG pages 71-72
Instruction
Read this situation to the class
Ask these questions:
  What went wrong?
  Could they have done something differently to get a different outcome? What could they have done differently?
  If you were part of this crew, would you have had any questions before starting the job? What are those questions?

## Slide 111
Pulling Pipe Criteria
SG 73
Pulling over pushing when possible
HDPE Pipe Handling Permit Required
Established procedures and controls
Notes: SG page 73
Instruction
Pulling over pushing when possible due to additional hazards created when pushing
An HDPE Pipe Handling permit is required to be completed prior to pulling pipe that meet this criteria:
  Greater than or equal to (≥) 2 inches in diameter, and
  Greater than (>) 50 feet
Sites must establish procedures and controls, such as rigging equipment, for pulling pipe that meet this criteria:
  Greater than or equal to (≥) 2 inches in diameter, and
  Less than (<) 12 inches in diameter

## Slide 112
Restrictions
SG 73
Pulling pipe up or down an incline
Notes: SG page 73
Instruction
Sometimes it is necessary to pull pipe up or down an incline
An Engineering Review is required for:
  Pulling pipe up or down grades greater than 25%
  Pulling pipe that is longer than 400 feet regardless of diameter

## Slide 113
Rigging
SG 74
Approved Rigging Assemblies Technical Supplements
Approved rigging form
HDPE Pipe 12 inches in diameter and larger
Notes: SG page 74
Instruction
Approved Rigging Assemblies Technical Supplements provide details for:
  Approved rigging that may be used for pulling pipe 12 inches in diameter and greater
  Rigging for pulling pipe that is greater than or equal to 2 inches in diameter and less than 12 inches in diameter must be defined in site procedures
Rigging forms
  Completed and approved are located on the DOHS SharePoint under the HDPE Pipe Handling folder
  Not in the approved folder, the rigging approval request must be completed and approved prior to use
HDPE Pipe 12 inches in diameter and larger
  Site shall use approved pipe rigging as defined in the HDPE Pipe Handling folder on the DOHS SharePoint
  If desired rigging is not listed, the HDPE Pipe Rigging Approval Request must be completed prior to using
  Rigging for pulling pipe that is greater than or equal to 2 inches in diameter and less than 12 inches in diameter must be defined in site procedures

## Slide 114
Rigging
SG 74-75
Rigging for multiple uses
Use of a sling as a “choker”
Pipe slotting
Notes: SG pages 74-75
Instruction
Rigging for multiple uses
  Ones for multiple uses must have:
    Approval request submitted to the Company PSST for approval
    Approved rigging
  Once rigging has been used for pulling pipe, it cannot be used for any other tasks other than pulling
  Rigging that has been used for pulling cannot be used for lifting
  Rigging must be marked to indicate what it has been used for to eliminate any confusion
Sling as a “choker”
  Not acceptable for pulling HDPE Pipe 12 inches in diameter or larger
  Including pulling lengths of pipe while fusing in a laydown area
  Is acceptable to use a sling to lift and position pipe (positioning a pipeline in a fusing machine or removing it from the machine)
Pipe slotting
  Pipe slotting (cutting a slot or shape into the pipeline to be used as an anchor point) is not acceptable for any pipe pulls regardless of diameter and length
  All equipment used for pulling HDPE Pipe will meet the pulling force requirements for the pull along with adhering to the rigging assembly specifications within the technical supplements

## Slide 115
Standard Dimension Ratio (SDR)
SG 75
SDR
Correlation (dimension and thickness)
Lower SDR
Higher SDR
Weight to be supported
Notes: SG page 75
Instruction
SDR term used when discussing the geometry of the HDPE Pipe and when rating piping pressure
Correlation between the pipe dimension and the thickness of the pipe wall
“A lower SDR ratio indicates that the pipe has a high-pressure rating because the pipe wall is thick compared to its diameter”
“A higher SDR ratio indicates that the pipe wall is thin compared to its diameter and therefore has a low-pressure rating”
SDR is used to determine the weight that the rigging and equipment must support (if needed, the references are in Student Guide, page 101)

## Slide 116
Proper Layout and Attachment
SG 76
Step 1
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 76
Instruction
The following is a step-by-step illustration for the proper layout and attachment of the rigging devices to the pipe and towing equipment for pulling HDPE Pipe stringer
Pipe shown has a 20 inch Nominal Pipe Diameter and a Pipe SDR Rating of 17.00
Table 2 from the Pipe Pulling Force Technical Supplement will be used to determine the pulling force for this pipe
Equipment will be able to pull the pipe up to a 25% grade
Pulling force is listed as 12,500 pounds
Scenario:
Use Rigging Assembly F
Assembly has a total working load limit of 50,000 lbs
From the chart on page 2 of the Rigging Assembly F Technical Supplement, rigging is approved for this scenario
Step 1:
  Ensure the pipe has been secured to prevent it from moving
  Lay out the center of the 2 inch or 2.5 inch diameter holes 10 inch from the end of the pipe
  Two holes will be drilled on opposite sides of the pipe from each other

## Slide 117
Proper Layout and Attachment
SG 76-77
Step 2
Level one text
  Level two text
  Level two text
Level one text
Notes: SG pages 76-77
Instruction
Step 2:
  Drill the (2) 2 inch or 2.5 inch holes in each side of the pipe
  A 2 inch or 2.5 inch Composite Core drill bit is recommended for this task
  Both holes are now drilled in the end of the pipe

## Slide 118
Proper Layout and Attachment
SG 78
Step 3
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 78
Instruction
Step 3:
Install first 2-inch shackle onto pipe
Insert shackle pin from the outside
Shackle weight is approximately 60 pounds
Get assistance when needed
Remember to use proper lifting techniques, watch for pinch points, and not drop shackles

## Slide 119
Proper Layout and Attachment
SG 78
Step 4
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 78
Instruction
Step 4:
Install the retainer in the shackle pin
Always install shackle pin so that retainer is on the inside to avoid damage

## Slide 120
Proper Layout and Attachment
SG 79
Step 5
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 79
Instruction
Step 5:
Thread a UTS10-95T x 5 foot round sling through the eyes in the end of the shackles

## Slide 121
Proper Layout and Attachment
SG 79
Step 6
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 79
Instruction
Step 6:
Install the remaining shackle on the other side
Repeat steps 3 and 4

## Slide 122
Proper Layout and Attachment
SG 80
Step 7
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 80
Instruction
Step 7:
Install a 1.5-inch screw pin shackle through the eyes of the sling
Connect the shackle to the eye of the 15 ton swivel
Connect the other end of the 15 ton swivel to the 1.5-inch master link

## Slide 123
Proper Layout and Attachment
SG 81
Step 8
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 81
Instruction
Step 8:
The completed rigging can now be attached to the towing vehicle
Be sure the tow vehicle being used has sufficient towing capacity for the load being pulled
This picture shows two clevises being used to anchor to the pulling equipment
Anchoring combinations may be used as long as they meet the minimum working load limit of an approved rigging assembly
This picture shows Assembly D with a working load limit of 50,000 pounds pulling capacity as defined in the technical supplement

## Slide 124
Proper Layout and Attachment
SG 81
Step 9
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 81
Instruction
Step 9:
When all connections are complete and all personnel are clear of the equipment, the pipe can be moved
This picture shows a completed pulling assembly secured to the pulling equipment.
Anchoring combinations may be used as long as they meet the minimum working load limit of an approved rigging assembly
Pulling equipment may have different anchor points to attach the pulling assembly
This picture shows Assembly D with a working load limit of 50,000 pounds pulling capacity as defined in the technical supplement

## Slide 125
Pipe Bending
SG 82
Creates additional stored energy
Things to consider
Notes: SG page 82
Instruction
Pipe bending creates additional stored energy
  The following must be considered when completing tasks:
    Minimum safe distances are determined
    Substantial barriers are provided when needed
    Appropriate equipment is selected

## Slide 126
Pipe Pull Requirements and Allowances
SG 82
Designated Blocking Equipment
Pulling Force
Working Load Limit
Notes: SG page 82
Instruction
Designated Block Equipment
  Only equipment allowed to pass the pipe being pulled
  To set up blocks along the path of travel
  Pipe is no longer in motion
  Proper passing communication procedures are followed
Pulling Force
  Is the amount of force required to pull the pipe based on the task conditions (i.e., diameter of pipe, SDR rating of pipe, and grade that the pipe will be moved)
  Required for a specific task can be found on Table 1 or 2 of the Pipe Pulling Force Technical Supplement
  If the pulling force required exceeds those found in Table 1 or 2, then an Engineering Review will be required
Working Load Limit
  Maximum rated pulling force that can be applied to the rigging equipment (i.e., “Rigging Assembly A” HDPE Fused Pulling Head, 5-Ton Swivel has a working Load Limit of 16,667 pounds)
  Never exceed the working load limit of the rigging assemblies

## Slide 127
Pipe Pull Requirements and Allowances
SG 82-83
Pipe Pulling Escorts
Flashing Blue Light
Notes: SG pages 82-83
Instruction
Pipe Pulling Escorts
  A Lead Escort and Trail Escort are required for:
    Pulling pipe
    There is the potential for interaction with other traffic
  Blocking is required any time other traffic could enter the path of the pipe pull
    Examples of blocking include
      Equipment with an operator blocking the road
      Appropriate use of flagging and/or barricading
  Two-way traffic
    Allowed if roads wide enough to maintain 50-foot safe zone around pipe
    Establish controls within the lane of travel
    Superintendent approval is needed for two-way traffic pulls
Flashing Blue Light
  Required on all equipment involved with pulling pipe where there is the potential for interaction with other traffic
  Must be easily visible during daylight hours

## Slide 128
HDPE Pipe Pulling Force
SG 83-84
Information Provided
Use with Approved Rigging Assemblies
Notes: SG pages 83-84
Instruction
The specific technical supplements that will be included in this module are:
  Pipe Pulling Force
  Approved Rigging Assemblies (A-F)
  Push/Pull/Positioning Illustrations
  Rigging Approval Request
There are exercises with scenarios to help all interact with these documents and get used to working with them.
The first one is the Pipe Pulling Force:
  Provides pulling force requirements over a range of pipe diameters and SDR ratings
  Pulling forces are based on pulling an empty 400-foot pipeline with a 0.8 coefficient of friction up a 17.5% grade (Table 1) and up a 25% grade (Table 2)
  Designed to be used in conjunction with the Approved Rigging Assemblies to:
    Assist in determining the appropriate rigging
    Associated equipment that can be used to safely perform the task

## Slide 129
Table 1
SG 85
Grade is 17.5% or less
Notes: SG page 85
Instruction
Table 1 is used for pulling pipe when the grade is 17.5% or less

## Slide 130
Table 2
SG 85
Grade is 25% or less
Notes: SG page 85
Instruction
Table 2 is used for pulling pipe when the grade is 25% or less
Ask the following questions. Discuss the answers, if needed.
What is the pipe pulling force for 16-inch pipe with SDR of 19 on a 25% grade?__________
What is the pipe pulling force for 20-inch pipe with SDR of 15.5 on a 17.5% grade? ________

## Slide 131
Approved Rigging Designs
SG 86-87
Subheading
Level one text
  Level two text
  Level two text
Level one text
Notes: SG pages 86
Instruction
The approved rigging designs for pulling HDPE Pipe are located on the DOHS SharePoint under H&S Policies, HDPE Pipe Handling
Each assembly consists of a two page document
First page of the document gives details about the assembly such as:
  The name of the rigging assembly - this is new to the technical supplement which helps to identify the rigging assembly
  Working load limit
  Results of the engineering review including a diagram of the assembly
  Parts list

## Slide 132
Assembly A Fused Head, 5-Ton Swivel
SG 87
Subheading
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 87
Instruction
This is one of the six currently approved rigging designs

## Slide 133
Assembly B Single 1 ½” Skookum Shackle, Bushing
SG 88
Subheading
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 88
Instruction
This is one of the six currently approved rigging designs

## Slide 134
Assembly C Fused Pulling Head, 15-Ton Swivel
SG 89
Subheading
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 89
Instruction
This is one of the six currently approved rigging designs

## Slide 135
Assembly D Two 1 ½” Skookum Shackles, 15-Ton Swivel
SG 90
Subheading
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 90
Instruction
This is one of the six currently approved rigging designs

## Slide 136
Assembly E Two 1 ½”, 2” Sch Bushing, 15-Ton Swivel
SG 91
Subheading
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 91
Instruction
This is one of the six currently approved rigging designs

## Slide 137
Assembly F Two 2” Skookum Shackles, 15-Ton Swivel
SG 92
Subheading
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 92
Instruction
This is one of the six currently approved rigging designs

## Slide 138
Scenario Example
SG 93
What assemblies can be used to pull a 30-inch pipe with an SDR rating of 26 up a grade of 16%?
Level one text
  Level two text
  Level two text
Level one text
Notes: SG page 93
Instruction
To answer this question
  Use the Pipe Pulling Force document to determine the pipe pulling force for the scenario
  The pipe is being pulled up a grade of 16%, use Table 1
Based on the information provided:
  30-inch pipe with an SDR of 26
  Pipe pulling force is 17,700 lbs
  Rigging assemblies A and B have a working load limit of 16,667 lbs. which is less than the requirement of 17,700 lbs
    Neither of these assemblies can be used
  Rigging assemblies C, D, E, and F have working load limits of 50,000 lbs
    These are potential rigging assemblies for this job
  Determine which of these assemblies can be used
    Look at the charts on page 2 of the Technical Supplements for each assembly
    Charts determine if the assembly can be used by considering factors other than the working load limit such as the wall thickness of the pipe

## Slide 139
Rigging Approval Request
SG 94
Notes: SG page 94
Instruction
For rigging not in the approved folder on the DOHS SharePoint, a Rigging Approval Request must be completed and approved prior to use
The HDPE Pipe Handling Rigging Approval Request provides the details of the rigging used to pull pipe 12 inches in diameter and greater

## Slide 140
Initial Information
SG 95
Notes: SG page 95
Instruction
Discuss the information in the red boxes

## Slide 141
Engineering Review and Summary
SG 95
Notes: SG page 95
Instruction
Discuss the information in the red boxes

## Slide 142
Shackle
SG 96
Notes: SG page 96
Instruction
Discuss the information in the red boxes

## Slide 143
Assembly Description and Diagram
SG 96
Notes: SG page 96
Instruction
Discuss the information in the red boxes

## Slide 144
Parts List
SG 97
Notes: SG page 97
Instruction
Discuss the information in the red boxes

## Slide 145
Approvals
SG 97
Notes: SG page 97
Instruction
Discuss the information in the red boxes

## Slide 146
Pipe Handling Illustrations
SG 98-100
Notes: SG pages 98-100
Instruction
The Pipe Handling Illustrations document demonstrates the differences between HDPE Pipe pulling, pushing, and positioning

## Slide 147
Directions
Fill in the chart using the HDPE Pipe Pulling Force and Approved Rigging Assembly Technical Supplements.
List all of the rigging assemblies that can be used for each scenario.
Plan It Out
Activity 5
SG 101
Notes: SG page 101
Time
Approximately 10 minutes
Materials
Student Guide
Pen/Pencil
HDPE Pipe Pulling Force chart
Approved Rigging Assembly Technical supplements
Purpose
This activity gives students the opportunity to practice planning for the working load limits and choosing an appropriate Rigging Design.
Instruction
Have the students fill in the chart on page 101 using HDPE Pipe Pulling Force and Approved Rigging Assembly Technical Supplements.
Go over the answers with them when they have completed the activity.
Answers:
  WL= 35,400; Rigging = C, D, E, & F
  WL= 37,500; Rigging = C, D, E, & F
  WL= 21,000; Rigging = C, D, E, & F
  WL= 16,200; Rigging = A & B
  WL= 28,900; Rigging = C, D, E, & F
  N/A- Engineering Review Required
[Note: Include directions that recognize varying class sizes by doing one of the following
Provide an activity where class size does not matter
Incorporate suggestions to slightly alter the given activity for larger and smaller than expected class sizes
Provide alternate activity for larger and smaller than expected class sizes]

## Slide 148
Debrief
What are some key concepts learned in this module?
What do you need to understand better?
What information surprised you?
Notes: SG N/A
Instruction
Discuss questions on slide

## Slide 149
Module 5: Fusing and Data Loggers
Notes: SG page 105
Instruction
Review learning objectives for the module
Upon completion of this module, students will be able to
  Identify the hazards associated with fusing, installation, and repair of HDPE Pipe as they relate to the FCX-HS12 policy and describe the proper procedures in place to mitigate those hazards

## Slide 150
Fusing Machines
SG 107-108
Stored Energy
HDPE Pipe Handling Permit
Significant Bends
Banding Clamps
Specifications and Standards
Notes: SG pages 107-108
Instruction
Stored energy sources
  Must be considered and controlled when loading and unloading pipe from a fusing machine
  Documented procedures will be established for fusing, installing, and repairing HDPE Pipe, in accordance with Policy expectations
An HDPE Pipe Handling Permit is required:
  For tasks involving fusing, installation, and/or repair for HDPE Pipe 2 inches in diameter and greater
  Where the final result of the task creates a pipe longer than 50 feet
Significant Bends
  A Qualified Individual must review tasks involving cutting pipe with significant bends
  A pre-job safety meeting will also be held to discuss hazards and precautions, and to determine safe distances, substantial barriers, and adequate equipment to perform the task safely
Banding Clamps
  It is important to remember banding clamps are not designed to splice the ends of two pipes together, and cannot prevent axial pipe movement
  Pipes should be fused or secured with a coupling designed for this application
Specifications and Standards
  Manufacturer specifications and applicable ASTM standards for fusing must be followed at all times
  If the specifications cannot be followed, or they do not exist for the pipe being used, an Engineering Review is required
  This includes the use of recycled HDPE Pipe

## Slide 151
Recording the Data – Data Loggers
SG 108
When data logging is used
Why data logging is used
Notes: SG page 108
Instruction
When data logging is used
  Data logging is required on all HDPE Pipe fuses involving HDPE Pipe 12 inches in diameter and greater
  Data logging on HDPE Pipe at smaller diameters is at site discretion, and should be considered in critical areas (such as high pressure installations, long-term installations, etc.)
  Data review process is at the discretion of each site
  Data logging does not guarantee the quality of a fuse
Why data logging is used
  A tool that assists operators with the pipe fusing process by providing fuse specifications and real-time process information for each fuse
  Helps to increase the likelihood of fuses meeting required specifications
  When fusing HDPE Pipe, there is specific information that must be captured and recorded
  This course is not designed to teach this process, as that will come in a later course
  It is important, though, to know what FCX-HS12 says about recording this data

## Slide 152
Hands-On Training
SG 108
Further HDPE education
Notes: SG page 108
Instruction
As per company need,
  Employees who take this class will continue their HDPE education within their sites
  Data Logging and Fusing will be separate classes that focus on the specific skills needed in those areas
  Going through this class does not qualify employees to work with the Data Loggers, nor to work with the fusing machines and fusing process
  If you have further questions, please contact your supervisor or training representative

## Slide 153
Directions
Partner up with another student
Read the “Learn From Others” scenario on SG p. 110
Discuss the results from the investigation found in the table
Use the questions on SG p. 109 to guide your discussion
Arm Chair Quarterback
Activity 6
SG 109-110
Notes: SG pages 109-110
Time
Approximately 10 minutes
Materials
Student Guide
Pen/Pencil
Purpose
This activity gives students the opportunity to use the information they have learned so far in analyzing a fatal scenario.
Instruction
Ask the students to pair up with a partner and read the scenario in their Student Guide, page 110
When finished reading the scenario, ask them to look at the breakdown of the investigation, Student Guide page 109 (Root Cause, Corrective Action)
These are the questions they should be asking and taking notes on, so as to discuss as a class:
  Do you agree with the findings? Did you think that anything else should have been included?
  If you were part of this team planning the job, what would you have done differently to ensure a safer outcome?
  Take notes below and be ready to discuss briefly with the class

## Slide 154
Quiz
Directions
Complete the quiz in the Student Guide (p. 111)
Discuss the answers as a class
Module 5 Quiz
SG 111
Notes: SG page 111
Instruction
Give students time to write answers to the quiz questions in the SG
Review the answers as a class using the slides

## Slide 155
Module 5 Quiz
SG 111
Stored energy sources must be considered and controlled when loading and unloading pipe from a fusing machine.
  True
  False
Notes: SG page 111
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, SG page 107

## Slide 156
Module 5 Quiz
SG 111
An HDPE Pipe Handling Permit is required for tasks involving fusing, installation, and/or repair for 2 inch diameter and greater HDPE Pipe where the final result of the task creates a pipe longer than 50 feet.
  True
  False
Notes: SG page 111
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, SG page 107

## Slide 157
Module 5 Quiz
SG 111
An Engineer must review tasks involving cutting pipe with significant bends.
  True
  False
Notes: SG page 111
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
b, SG page 107

## Slide 158
Module 5 Quiz
SG 111
Banding clamps are designed to splice the ends of two pipes together.
  True
  False
Notes: SG page 111
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
b, SG page 108

## Slide 159
Module 5 Quiz
SG 111
Manufacturer specifications and applicable ASTM standards for fusing must be followed at all times.
  True
  False
Notes: SG page 111
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, SG page 108

## Slide 160
Module 5 Quiz
SG 111
Data Logging guarantees quality fusing of HDPE Pipe.
  True
  False
Notes: SG page 111
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
b, SG page 108

## Slide 161
Debrief
What are some key concepts learned in this module?
What do you need to understand better?
What information surprised you?
Notes: SG N/A
Instruction
Discuss questions on slide

## Slide 162
Module 6: Audits and Training
Notes: SG page 115
Instruction
Review learning objectives for the module
Upon completion of this module, students will be able to
  Define the roles and responsibilities of the Corporate and site Pipe Safety Steering Teams
  Explain the training requirements needed to safely handle or participate in the handling of HDPE Pipe

## Slide 163
Corporate Team
SG 117
Pipe Safety Steering Team (PSST)
Members
Visits
Meetings
Notes: SG page 117
Instruction
Pipe Safety Steering Team (PSST)
  Comprised of representatives from each area/site affected by this policy
  Oversees the policy for each FCX business unit, and a site team ensures best practices are being followed at each site
  Evaluates existing standards, set new guidelines, and monitor site performance
Members
  Will consist of these Freeport-McMoRan Inc. employees:
    Sponsor – Manager, GM, or Director Level
    Lead – Superintendent or Manager Level
    Site Champions
    Global Sourcing Representative
    Health and Safety Representative
    Engineering Representative
    Training Representative
Visits
  Annual site visits at each branch to:
    Monitor compliance
    Look for best practices
    Provide feedback for improvement
  Include compliance with this policy, training, procedures, and field practices
Meetings
  Quarterly meetings
  All members review practices and make recommendations for change where needed
  Changes to the current policy and appendices must:
    Go through a formal approval process with the PSST
    Be brought back to site teams for implementation

## Slide 164
Site Teams
SG 117
Members
Field Audits
Notes: SG page 117
Instruction
Members
  Comprised of the following Freeport-McMoRan Inc. employees:
    The Site Champion (member of the company’s PSST)
    Engineering Representative
    Global Sourcing Representative
    Health and Safety Representative
    Representative from Each Affected Area
Field Audits
  Conducted by Site Teams to:
    Ensure pipe handling practices are being followed
    Identify any improvement opportunities
    Take place at minimum once per quarter

## Slide 165
Low-Frequency Usage Sites
SG 118
Use other sites
Implement Policy
Notes: SG page 118
Instruction
Sites that handle HDPE Pipe on a minimal basis or as part of short duration projects will:
  Utilize expertise from other sites to assist with review of the project
  Implement the policy prior to work commencing

## Slide 166
Training
SG 118
Training Format
Refresher
Notes: SG page 118
Instruction
All employees and contractors who handle or participate in the handling of HDPE Pipe must be trained on this policy
Training includes the hazards associated with the handling of HDPE Pipe and how to effectively complete the forms associated with the policy
Training Format
  Interactive
  Consist of classroom
  Video
  Field demonstration of the task
  Employees must demonstrate competency (both verbal and visual) to assess understanding
  Existing site documents and skills assessment formats may be utilized, but must include the skills listed in the FCX Skills Assessments
Refresher
  All employees trained on this policy must receive refresher training every year
  At a minimum, the training will include the key elements listed in this section:
    Use of the HDPE Pipe Handling Permit
    Determination of safe distances to position employees from pipe during movement or after movement and proper use of substantial barriers
    Review by a qualified individual of piping that is found to contain residue or solution
    Specific rigging task training for pipe handling and pulling
    Unloading, loading, and storage of HDPE Pipe
    HDPE Pipe pulling and handling
    Fusing HDPE Pipe
    Inspections of pipe and prevention of hazards and failures
    Incident review and potential hazards and problem areas
    Mobile equipment used for HDPE Pipe handling

## Slide 167
Training
SG 119
Skills Assessment
Documentation
Records
Notes: SG page 119
Instruction
Skills Assessments will be used for determining qualified individuals on a task-basis
Sites will utilize site specific training as well as the skills assessments developed by the PSST to evaluate individuals and verify competency prior to working with HDPE Pipe
Skills shall include:
  Hazard identification
  Hazard control procedures
  Safe operation of equipment
Skills assessments will be utilized to qualify individuals to:
  Train/mentor others
  Perform tasks
  Complete permits for the areas listed below:
    HDPE Pipe Handling Policy
    HDPE Pipe Handling Permit
    General Equipment HDPE Pipe Handling
    General Pipe Selection and Identification
    HDPE Pipe Unloading, Loading, and Storage
    Pulling Pipe
    Rigging Equipment
    Pipeline PM and Inspection
    HDPE Pipe Unrolling
    Flow Isolation and Distribution
    Fusing and Fusing Equipment
Documentation
  All training will be documented, including a training matrix with employee skills, and will be kept readily available/accessible
Records
  The following records must be retained according to the FCX Records Retention Policy:
    HDPE Pipe Handling Permits
    HDPE Pipe Handling Engineering Reviews
    HDPE Pipe Loading/Unloading Checklist
    HDPE Pipe Handling Rigging Approval Requests

## Slide 168
Directions
Pick a partner
Together, discuss and write answers to the Frequently Asked Questions
Use the policy as your guide for answering the questions
Be ready to discuss your answers with the class
Frequently Asked Questions
Activity 7
SG 120
Notes: SG page 120
Time
Approximately 10 minutes
Materials
Student Guide
Policy
Pen/Pencil
Purpose
This activity gives students the opportunity to apply their knowledge of FCX-HS12 to find answers.
Instruction
Have students pair up
Have the students use their Policy (FCX-HS12) to answer these questions
Answers:
Policy 3.2 & Technical Supplements
Policy 3.2 & Technical Supplements
Policy 3.2 & Technical Supplements
Policy 2.1
Policy 2.0 & 2.1
Policy 3.1 & Receiving/Loading/Unloading Checklist
Policy 5.0

## Slide 169
Quiz
Directions
Complete the quiz in the Student Guide (p. 121)
Discuss the answers as a class
Module 6 Quiz
SG 121
Notes: SG page 121
Instruction
Give students time to write answers to the quiz questions in the SG
Review the answers as a class using the slides

## Slide 170
Module 6 Quiz
SG 121
What does PSST stand for?
P______ S______ S______ T______
Notes: SG page 121
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
Pipe Safety Steering Team, SG page 117

## Slide 171
Module 6 Quiz
SG 121
The Corporate PSST is responsible to do the following: (Circle all that apply)
  Oversee the policy for each FCX business unit
  Site visits
  Field Audits
  Identify site improvement opportunities
  Monitor compliance with FCX-HS12
  Annual Site Audits
Notes: SG page 121
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
a, b, e, f, SG page 117

## Slide 172
Module 5 Quiz
SG 121
The Site PSST is responsible to do the following: (Circle all that apply)
  Oversee the policy for each FCX business unit
  Site visits
  Field Audits
  Identify site improvement opportunities
  Monitor compliance with FCX-HS12
  Quarterly Site Audits
Notes: SG page 121
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
c, d, e, f, SG page 117

## Slide 173
Module 5 Quiz
SG 121
Once you are trained to FCX-HS12, how often will you need to take a refresher training?
  Quarterly
  Annually
  Biannually
  Monthly
Notes: SG page 121
Instruction
Discuss answer as a class
Click to circle the answer
Quiz Answer
b, SG page 118

## Slide 174
Debrief
What are some key concepts learned in this module?
What do you need to understand better?
What information surprised you?
Notes: SG N/A
Instruction
Discuss questions on slide

## Slide 175
Conclusion
Notes: SG N/A
Instruction
The conclusion covers
Course review
Assessments
Student Course Evaluation
Facilitator Course Evaluation

## Slide 176
Conclusion
SG 133
FCX-HS12
Company Pipe Safety Steering Team (PSST)
Safety – who is responsible?
Notes: SG page 133
Instruction
FXC-HS12
High Density Polyethylene Pipe must be handled with careful planning and care, as it has the potential to have an enormous amount of stored energy
Developed policy FCX-HS12, to give instruction and guidance to all sites who have a business need to use HDPE Pipe.
PSST
The Company Pipe Safety Steering Team (PSST) will:
  Conduct annual site visits to each site to monitor compliance
  Look for best practices
  Provide feedback for improvement
The HDPE Pipe Handling Policy has been created to ensure past incidents involving the handling of HDPE Pipe will not be repeated and provide a path to improve upon successes
With careful planning and compliance, all can work safely when handling HDPE Pipe
Safety
We are all responsible for our own safety, as well as our coworkers
Remember if conditions change, or if something does not appear safe, anyone has the right to stop the job and ask for additional planning and problem-solving to take place
It is our goal that everyone go home safely

## Slide 177
Debrief
What are some of the key concepts in each module?
  Module 1: Introduction
  Module 2: Risk Management
  Module 3: Pipe Handling
  Module 4: Rigging
  Module 5: Fusing and Data Loggers
  Module 6: Audits and Training
Are there any additional questions, comments, or concerns?
Notes: SG N/A
Instruction
As objectives for each module are reviewed, discuss the students’ lingering questions, comments, or concerns
Module 1
  Describe the history and purpose behind FCX-HS12
Module 2
  Describe the purpose and process for hazard recognition before performing tasks related to working with HDPE Pipe
  Identify the personnel who will be associated with the task, as well as their roles and responsibilities, to ensure the task is being performed safely and all involved abide by the policy
Module 3
  Describe safe practices and requirements of FCX-HS12 regarding receiving, loading, unloading, and storage of HDPE Pipe on FCX properties
  Identify when to use the Receiving/Loading/Unloading Checklist, and describe how to fill out this form correctly
  Identify the difference between a properly loaded shipment of HDPE Pipe and one that does not comply with the company’s shipping standards
  Describe the procedure in place to report loads that do not meet company standards
  Describe how to safely store HDPE Pipe according to policy requirements
Module 4
  Describe the proper procedures required to safely pull various sizes and lengths of HDPE Pipe according to policy requirements
  Identify the proper equipment required for the task
  Identify appropriate forms for the tasks that will be performed and describe how to fill these forms out correctly
Module 5
  Identify the hazards associated with fusing, installation, and repair of HDPE Pipe as they relate to the FCX-HS12 policy and describe the proper procedures in place to mitigate those hazards
Module 6
  Define the roles and responsibilities of the Corporate and site Pipe Safety Steering Teams
  Explain the training requirements needed to safely handle or participate in the handling of HDPE Pipe

## Slide 178
Assessment
Directions
Complete the assessment
Return the completed assessment to the facilitator
Facilitator scores the assessment
Knowledge Assessment
Notes: SG N/A
Instruction
Students complete the knowledge assessment
Use the Answer Key to score each assessment

## Slide 179
Assessment
Directions
Read through the student directions
Complete the assessment while the facilitator observes
Performance Assessment
Notes: SG N/A
Instruction
Students complete the performance assessment according to the directions on the Performance Assessment documents
Score the performance assessment according to the directions on the Performance Assessment documents

## Slide 180
Evaluation
Directions
Complete the Course Evaluation in the Student Guide (p. 133)
Carefully tear out the evaluation
Return the completed form to the facilitator
Student Course Evaluation
SG 133
Notes: SG page 133
Instruction:
Students complete the Student Course Evaluation (in SG)
Collect and return evaluations (including the Facilitator Course Evaluation in the back of the FG) to the Mine Training Institute according to the directions on the form