## Slide 1
Air Monitor (MX4 Ventis)
Date 2019

## Slide 2: Ventis MX4 Air Monitor

## Slide 3: Instrument Buttons
Power Button
Press to view information and access utilities.
Press and hold to power on or off the instrument.
Enter
Press to start a utility.

## Slide 4: Start up
Press and hold the power button to start the monitor
Monitor will scroll through display screens

## Slide 5: 4 STEPS OF OPERATION
Bump Test
  Ensure bump test has been done
Check Battery Status
  Fully charged
Zero Sensors
  Use power to scroll through utilities and press enter at the Zero Sensor screen
Clear Peaks
  Use power to scroll through utilities and press enter at the Peaks screen

## Slide 6: Sensors Installed
SO2 Sulfur Dioxide
O2 Oxygen
NO2 Nitrogen Dioxide
Notes: SO2 = 2 PPM (OEL) H2O = 10 PPM (OEL) O2 = 19.5% - 23.5% (OEL) NO2 = 0.2 PPM (OEL)
SO2 = 100 PPM (IDLH) H2O = 10 PPM (IDLH) O2 = 19.5% - 23.5% (IDLH) NO2 = 0.2 PPM (IDLH)

## Slide 7: Sulfur Dioxide Hazards
Sulfur Dioxide (SO2):
  Very toxic, can cause death
  Can cause severe irritation of the nose and throat
  Can cause accumulation of fluid in the lungs (pulmonary edema)
  This gas can form from the head space of any sulfuric acid storage tank

## Slide 8: Sulfur Dioxide (SO2)
Effects of Various SO2 Levels | 
Sulfur Dioxide Level in PPM | Resulting Conditions on Humans
2 | The allowable exposure based on an 8 hour work shift (OEL)
0.3-1 | Sulfur Dioxide initially detected by taste
3 | Odor becomes easily detected
6-12 | Irritation of the nose and throat
20 | Irritation of the eyes
100 | Immediately Dangerous to Life or Health (IDLH)
400-500 | Dangerous concentration can cause edema (excess fluid in the lungs) and death from prolonged exposure
Source: Dangerous Properties of Industrial Materials (Sixth Edition) by N. Irving Sax
Notes: Explain a few symptoms that employees can detect from the following levels.

## Slide 9: Nitrogen Dioxide Hazards
Nitrogen Dioxide (NO2):
  Reddish-brown gas with a pungent, acrid odor
  Irritation eyes, nose, throat
  Increased inflammation of the airways
  Sulfuric acid containing high nitrates when diluted can create Nitrogen Dioxide

## Slide 10: Nitrogen Dioxide (NO2)
Effects of Various NO2 Levels | 
Nitrogen Dioxide Level in PPM | Resulting Conditions on Humans
0.2-1 | Detectable by pungent, acrid odor
0.2 | The allowable exposure based on an 8 hour work shift (OEL)
5 C | Ceiling Limit = exposure limit not to be exceeded for any length of time
5-10 | Irritation of the nose and throat
20 | Immediately Dangerous to Life or Health (IDLH)
Source: Dangerous Properties of Industrial Materials (Sixth Edition) by N. Irving Sax
Notes: Explain a few symptoms that employees can detect from the following levels.

## Slide 11: Oxygen (O2)
Effects of Various O2 Levels | 
Concentration Of Oxygen in % Volume | Resulting Conditions on Humans
23.5 | Maximum "Safe Level"
21 | Oxygen Concentration of AIR (20.954%)
19.5 | Minimum "Safe Level"
17 | Impairment of judgment starts to be evident
16 | First signs of Anoxia - results when oxygen is not being delivered to a part of the body
16-12 | Breathing and pulse rate increases, muscular co-ordination is slightly impaired
14-10 | Consciousness continuous; emotional upsets, abnormal fatigue upon exertion, disturbed respiration
10-6 | Nausea and vomiting, inability to move freely and loss of consciousness may occur
<6 | Convulsive movements and gasping respiration occurs; respiration stops and a few minutes later heart action ceases
Source: Industrial Scientific 2014 – The Gas Detection People
Notes: Explain a few symptoms that employees can detect from the following levels.

## Slide 12: Oxygen Hazards
Oxygen (O2):
  Levels below 19.5% oxygen shall be considered as oxygen deficient and hazardous
  Oxygen content over 23.5% shall be considered oxygen enriched and hazardous, entry shall not be made